## Slide 1
Chemical process industries
lecture 2
HNO3 production
By
Dr.Intisar Khalaf

## Slide 2
NITRIC ACID
INTRODUCTION
Nitric acid (HNO3), also known as aqua fortis (strong water) and spirit of niter, is
a highly corrosive strong mineral acid.
The pure compound is colorless, but older samples are yellowish in color due to the accumulation of oxides of nitrogen.
Commercially available nitric acid having concentration of 68% HNO3, while the solution containing more than 86% HNO3, is referred to as fuming nitric acid.
Depending on the amount of nitrogen dioxide present, fuming nitric acid is further characterized as white fuming nitric acid or red fuming nitric acid, at concentrations above 95%.
Commercial grade of HNO3
36 Be sp.gr 1.33 52.3%
40 Be sp.gr 1.381 61.4%
42 Be sp.gr 1.408 67.2%

## Slide 3
MANUFACTURE
Nitric acid is manufactured by three methods.
1. From Chile saltpetre or nitrate
2. Arc process or Birkeland and eyde process
3. Ostwald's process or Ammonia oxidation process
1. From Chile saltpeter or nitrate
It is the first commercial process of manufacture of nitric acid from sodium nitrate extracted from Chile saltpeter. The process is now become obsolete since second decade of nineteenth century.
Raw materials
Sodium Nitrate
Sulfuric acid
Sources of raw material
Sulfuric acid can be obtained by contact process.
Sodium nitrate can be obtained from caliche ore. Also, it is manufactured by neutralization of soda ash with nitric acid as well by reaction of ammonium nitrate and sodium hydroxide.
Reaction
NaNO3 + H2SO4 NaHSO4 + HNO3

## Slide 5
2. Arc process or Birkeland and eyde process:
N2+O2 2NO endo.
2NO+O2 2NO2
4NO+H2O HNO3
3. Ostwald's process or Ammonia oxidation process:
Raw Materials
Ammonia
Air
Platinum
Water
Steam credit
Power
Reaction
Major reactions
4NH3 + 5O2 4NO + 6H2O ΔH = - 216.6kcals ---- (1)
2NO+O2 2NO2 ΔH = - 27.1kcals ---- (2)
3NO2+H2O 2HNO3+NO ΔH = - 32.2 kcals .... (3)
NH3+O2 N2O + H2O ΔH = - 65.9kcals ... (4)

## Slide 6
Manufacture
Nitric acid is made by the oxidation of ammonia, using platinum or platinum- 10% rhodium as catalyst, followed by the reaction of the resulting nitrogen oxides with water.

## Slide 7
Compressed air is mixed with anhydrous ammonia, fed to a shell and tube convertor designed so that the preheater and steam heat recovery boiler-super heater are within the same reactor shell. The convertor section consists of 10-30 sheets of Pt-Rh alloy in the form of 60-80 mesh wire gauge packed in layers inside the tube. Contact time and of the gas passes downward in the catalyst zone 2.5 X 10-4sec and are heated at 8000C.
Product gases from the reactor which contain 10-12% NO, are sent through heat recovery units consisting of heat recovery boiler, super heater and quenching unit for rapid cooling to remove large fraction of product heat, and into the oxidizer-absorber system. Air is added to convert NO to NO2 at the more favourable temperature (40-500C) environment of the absorption system.
The equipment in the absorption train may be series of packed or sieve tray vertical towers or a series of horizontal cascade absorbers. The product from this water absorption system is 57- 60% HNO3 solution which can be sold as or concentrated as follow:
Concentration by H2SO4
Concentration by Mg(NO3)2

## Slide 9
The process involves four steps
Catalytic oxidation of ammonia with atmospheric oxygen to yield nitrogen monoxide .
2. Oxidation of the nitrogen monoxide product to nitrogen dioxide or dinitrogen tetroxide.
3. Absorption of the nitrogen oxides to yield nitric acid.
4. Concentration of nitric acid .
Catalyst for oxidation of ammonia
Platinum/rhodium alloy containing 10% rhodium is the only industrially viable catalyst.
Rhodium not only improves the catalytic properties of platinum but also improves mechanical and anti-abrasive properties of material under the operating condition such as to counter the severe corrosion and oxidation atmosphere.
4–10 % of rhodium used in Pt/Rh supported catalyst. Higher efficiencies and smaller platinum losses can be achieved by knitted gauzes.

## Slide 10
The metallic alloy catalyst is prepared into very fine threads of diameter 0.05mm which are woven into meshes with more than 1000stiches/cm2. Two to four or even more of these meshes are placed on top of one another inside the reactors when these are put into operation.
Catalyst threads are smooth, bright and less active at initial stage, as the time progresses they becomes dull and wrinkled whereupon their activity rises to the maximum. Finally they become spongy with activity falling off.
When it is in most active state, ammonia oxidation yields up to 98% of NO are obtained.
Ammonia conversion efficiency is a function of pressure and temperature.
As the pressure increases, higher temperatures are needed to obtain the high conversion efficiency.

## Slide 11
An increased flow rate and the presence of several layers of the catalyst help to minimize undesirable side reactions. However, high flow rates increase the catalyst loss which leads to search for non-platinum catalysts for ammonia oxidation. The most prospective non-platinum catalysts are based on oxides of Co, Fe or Cr.
Catalyst poison
Sulfates, H2S, chlorides, Arsenic and its oxide, Si, P, Pb, Sn and Bi are permanently poisoning the catalyst. These elements lead to the formation of inactive compounds in the wires resulting in decreasing of the catalytic activity.
Traces of acetylene, ethylene, Cr, Ni and Fe temporarily reduce the conversion efficiency which can be restored by treatment with HCl. There so air should be freed from all above impurities along with suspended particles of lubricants, fats, fine dust and abrasive powder. Also, suspension of Fe2O3 from ammonia is removed. For that efficient filtration system along with magnetic separators are provided.

## Slide 12
PROPERTIES
Physical Properties
 Molecular formula : HNO3
 Molecular weight : 63.013gm/mole
 Appearance : Colourless liquid
 Odour : Pungent
 Boiling point : 121ºC (68% HNO3 solution)
 Melting point : -42ºC
 Density : 1.5129gm/mL (liquid)
 Solubility : Miscible with water in all proportions
 The impure nitric acid is yellow due to dissolved oxides of nitrogen, mainly NO2.
 It has a corrosive action on skin and causes painful blisters.
Chemical Properties
 Acidic properties: It is a strong monobasic acid and ionization in aqueous solution.
 Oxidizing properties: It acts as a powerful oxidizing agent, due to the formation of nascent oxygen.
 Action on metals: It reacts with almost all the metals, except noble metals, like Pt and Au. The metals are oxidized to their corresponding positive metal ions while HNO3 is reduced to NO, NO2. N2O, NH2OH or NH3, depending upon the conditions such as temperature, nature of metal and concentration of the acid.
 Nitric acid has ability to separate gold and silver.

## Slide 13
USES
 As a starting material in the manufacture of nitrogen fertilizers such as ammonium nitrate, ammonium phosphate and nitrophosphate. Large amounts are reacted with ammonia to yield ammonium nitrate.
 Weak acid are used to digest crude phosphates.
 As a nitrating agent in the preparation of explosives such as TNT, nitroglycerine, cellulose polynitrate, ammonium picrate
 In manufacture of organic intermediates such as nitroalkanes and nitroaromatics.
 Used in the production of adipic acid.
 Used in fibers, plastics and dyestuffs industries
 Used in metallurgy and in rocket fuel production
 As the replacement of sulfuric acid in acidulation of phosphate rock.