## Slide 2: Chemical Composition of Petroleum
Petroleum is a mixture of hundreds of hydrocarbons of all type with water, salts, sulfur and nitrogen containing compounds and some metal complexes.
The elementary composition of crude oil usually falls within the following ranges.
The three different types of hydrocarbons that crude has are paraffins, aromatics, cyclo-alyphatic or naphthenes and olefins.

## Slide 3
Paraffins
The paraffin series of hydrocarbons is characterized by the rule that the carbon atoms are connected by a single bond and the other bonds are saturated with hydrogen atoms. The general formula for paraffins is CnH2n+2. The simplest paraffin is methane, CH4, followed by the homologous series of ethane, propane, normal and isobutane, normal, iso-, and neopentane, etc. (Fig. 1).
Figure( 1 ) Paraffins in crude oil.

## Slide 4
Saturated alkanes: (n-alkane and i-alkane)
General formula CnH2n+2
Boiling point and density increase with increasing # of C atoms.
Branched alkanes (iso-alkanes) is very small in quantity
Boiling point of straight chains > iso-alkanes with the same # of C

## Slide 5
Naphthenes or cycloparaffins
Cycloparaffin hydrocarbons in which all of the available bonds of the carbon atoms are saturated with hydrogen are called naphthenes. Typical examples of these are cyclopentane, cyclohexane, etc. (Figure 2). General formula CnH2n for one ring compounds
Figure 2: Naphthene compounds

## Slide 6
Aromatics
The aromatic series of hydrocarbons is chemically and physically very different from the paraffins and cycloparaffins (naphthenes). Aromatic hydrocarbons contain a benzene ring which is unsaturated but very stable and frequently behaves as a saturated compound. Some typical aromatic compounds are shown in (Figure 3).
Figure 3: Aromatic compounds

## Slide 7
Olefins
Olefins do not naturally occur in crude oils. However, they are formed during its processing. They are very similar to paraffins, but they exhibit double bonds, usually one per molecule (Figure 4), although some di-olefins (two double bonds in the same molecule, ( Figure 5) can be found.
Figure 4: Olefin compounds
Figure 5: Di-olefin compounds

## Slide 8
Heteroatom compounds
Sulfur compounds might be present in inorganic and organic forms. In crude oils sulfur concentration can range from 0.1 to more than 8 weight percent. Such as dibenzylthiophene (2 benzene rings separated by 1 S atom) – is most difficult to relase the Sulfur
Oxygen compounds are responsible for petroleum acidity in particular.
Carboxylic (OH-C=O bonded to a benzene ring)
Phenolic (OH bonded to a benzene ring)
Nitrogen compounds
carbazole (2 benzene rings separated by 1 N atom) – neutral
Quinoline (2 benzene rings with 1 N atom on 1 ring) - basic
Metal Compounds
Porphyrins contain Ni, V, or Fe