## Slide 1
Petroleum Refinery

## Slide 2: The Petroleum Refinery
A small refinery: will take in
2000 to 10000 tons of crude oil/ day .
A large refinery: 20000 to 40000 tons/day and these are a few refineries larger than this up to 60000 tons/day.
Refineries vary in complexity ;i.e. in the variety of processes operated and of products that are sent out.

## Slide 3: Simple refinery : may make only gasoline, diesel fuel, and heavy fuel. The crude oil is distilled into: 1) Gaseous hydrocarbons, which are burnt as refinery fuel. 2) Light gasoline, which will need sweetening, a simple chemical treatment, and then use for automotive use except for its low octane number. 3) Naphtha of very low octane number, perhaps 40 compared with a market of 90. It is catalytically reformed, by which octane number of 90 to 95 can be obtained.
Petroleum Refinery

## Slide 4: A simple refinery consist of : a crude oil distilling unit, a gasoline sweetening unit and a catalytic reformer. Refineries having just this usually small of 2000 to 4000 tons/day of crude oil. >> Next stage of complexity is to added a desulphurization unit to treat the diesel fuel. >> Usually also the growing refinery will make (LPG) and some low grade kerosene. >>The kerosene will also need refining, at least sweetening to make it of marketable odor.
Petroleum Refinery

## Slide 5
Large Complex Refinery: will have many more units
representing more processes.
Petroleum Refinery
a) Vacuum Distillation
b) Hydro-cracking
c) Catalytic Cracking
d) Wax Plant
e) Sweetening and
Desulphurisation
f) Alkylation unit
g) Lubricating oil refining

## Slide 6: a) Vacuum Distillation : To make a heavy distillate suitable for catalytic cracking or hydro-cracking or manufacture of lubricating oils , and a residue which may be blown or further distilled for bitumen. b) Hydro-cracking : which makes more naphtha for catalytic reforming, more diesel fuel and low sulphur fuel. c) Catalytic Cracking : which makes much gas, suitable for LPG ; olefinic hydrocarbons, the feed stock for many petroleum chemicals ; and high grade gasoline. d) Wax Plant : de-waxing to get wax out of oil, then de oiling of the crude wax and final purification of the wax by hydrogenation.
Petroleum Refinery

## Slide 7: e) Sweetening and Desulphurisation : for jet fuel. f) Alkylation unit : to synthesize very high octane components for gasoline out of by product gases from processes (b) , (c) and the primary distillation of the crude oil. g) Lubricating oil refining : special plant to remove resinous and solidifying materials from lubricating oil stocks and achieve the finished product by blending.
Petroleum Refinery

## Slide 8: Butane and ltr → gas unit for refining and separation Gasoline → Blending Naphtha → Reforming Kerosene → Hydrogenation Light Gas oil → Gas Oil Blending Heavy Gas oil → Catalytic Cracking Reduced Crude → Vacuum Distillation Unit
Petroleum Refinery
Butane and ltr
Gasoline
Naphtha
Kerosene
Light Gas oil
Heavy Gas oil
Reduced Crude
C.O.

## Slide 9: Gas It is from petrolum is classified under several names:-
Petroleum Refinery
a) Natural gas
b) Associated gas
c) Dissolved gas
d) Refining off gas
e) Liqiuified Petroleum Gas (LPG)

## Slide 10: a) Natural gas : It is readily a vailble in nature, in almost as a finished product. It contains mainly methane It may be accompanied by other dry fractions like ethane and propane to a small extent. In addition to these combustibles some inerts like CO2 ,N2 , noble gases are also present. The proportion of methane ranges from 85% to 98%. b) Associated gas : This is obtained from oil reservoirs and this exists as a separate gas cap over liquid phase. The proportion of CH4, C2H4 , C3H8 vary depending on reservoir conditions. When the gas phase is taken out, it may still contain some liquid , hyrocarbons mainly of volatile range like butane and pentane which when condensed are treated as (Natural Gasoline ).

## Slide 11: c) Dissolved gas : Gas may be present in liquid HC mainly in the dissolved state depending upon the formation pressure. When the pressure decreased, this dissolved gas comes out of the oil. This gas is separated before transportation in pipe lines or tankers . The remaining is first to come out of the distillation column because of higher temperature. d) Refining off gas : In refinery , gas is formed in cracking and reforming operations due to the thermal degradation of liquid hydrocarbons. During stabilization of wild gasolines or possessed gasolines, the gases are vented. This forms a major source of heat energy for refinery, as wall as feed stock for petrochemicals.
Petroleum Refinery

## Slide 12: All the gases contain impurities like CO2 ,N2 , mercaptans, H2S, water vapor, suspended impurities. First three paraffin are gases at room temperature. The mixture of methane and ethane is called dry gas , propane and butane mixture is called wet gas. e) Liquefied Petroleum Gas (LPG) : Propane is frequently used as LPG after being mixed with butane. The most important property of this fuel is the vapor pressure. For factiliting leak detection, the gas is mixed with small amount of odourous mercaptans.
Petroleum Refinery

## Slide 13: Gasoline Most refiners produce gasoline in two grades, regular and premium and in addition supply a low-lead or non-lead gasoline to comply with antipollution requirements. The principal difference between regular and premium fuels is the antiknock performance. Gasoline is a complex mixture of hydrocarbons C4-C12 having a boiling range from 100 to 400 oF as determined by ASTM method. Components are blended to promote : 1) high antiknock property. 2) ease of starting. 3) quick warm-up. 4) low tendency to vapor lock. 5) low engine deposits.
Petroleum Refinery

## Slide 14: Normal butane is blended into gasoline to give the desired vapor pressure which is a compromise between high RVP to improve starting characteristics and a low RVP to prevent vapor lock and reduce evaporation losses. As butane has a high blending octane number as much as vapor pressure limitation permits.
Petroleum Refinery

## Slide 15: Gasoline specifications The most important properties are : 1) Boiling Range 2) Antiknock Properties 1) Boiling Range: - This governs ease of starting - rate of acceleration - loss by crankcase dillution. - and tendency towards vapor lock. Engine warm-up time is affected by the % distilled at 158 oF and the 90% ASTM distillation temperature. Warm up is expressed in terms of the miles of operation required to develop full power without excessive use of the choke.
Petroleum Refinery

## Slide 16: Crankcase dilution is controlled by the 90% ASTM distillation temperature and is also a function of outside temperature. Tendency to vapor lock is directly proportional to the RVP of the gasoline. RVP is approximately the vapor pressure of the gasoline at 100 oF in Lb/in2 absolute.
Petroleum Refinery

## Slide 17: 2) Antiknock Properties : There are two types of octane numbers for gasoline engines, those determined by: The motor method (MON) The research method (RON) Both methods use the same basic test engine but operate under different conditions. The RON represents the performance during low-speed driving when acceleration is relatively frequent, and the MON is a guide to engine performance and high speeds or under heavy load conditions. - The difference between the RON & MON of gasoline is an indication of the change of performance under both city and highway driving and is known as the "sensivity" of the fuel.
Petroleum Refinery

## Slide 18: Distillate Fuels: 1) Jet Fuels. 2) Diesel Fuels. 3) Heating Oils. 1) Jet Fuels : Commercial jet fuel is a material in the kerosene boiling range and must be clean burning. One of the critical specification of jet fuels is its smoke point and this limits the % of cracked products high in aromatic that can be incorporated. Specification limit the aromatic conc. to 20%. Hydrocracking saturates the aromatics in the cracked products and raise the smoke point.
Petroleum Refinery

## Slide 19: The freeze point specification is very low (-40 oF to -58 oF) max. and hydrocracking is also used to isomerize paraffins and lower the freeze point. In addition the other limiting specification is flash point (110 to 150 oF). Naphtha jet fuel is produced for military and is a wide- boiling- range stock which extends through the gasoline and kerosene boiling range. 2) Diesel Fuels : The major performance characteristics of diesel fuels, some what in the order of importance are : (cleanlines, ignition quality, volatility, viscosity)
Petroleum Refinery

## Slide 20: No.1 diesel fuel : is generally made from virgin stocks having cetane No. above 50 . It has a boiling range from 360 to 600 oF (250 to 320 oC) and is used in high- speed engines in trucks and buses, it is called some time super diesel. No.2 diesel fuel : is similar to No.2 fuel oil, and has a wider boiling range (350 to 650 oF) than No.1. It is usually contains some cracked stocks and may be blended from naphtha, kerosene , and light cracked cycle oils.
Petroleum Refinery

## Slide 21: Limiting specifications are Flash point ( 120 to 125 oF min.) 5% 0.5% max Dist. Range Cetane No. (52 min.) Pour point (-10 to +10 max.) The ignition properties of diesel fuels are expressed in terms of cetane number which expressed the volume % of cetane (C16H34 , high ignition quality) in a mixture with alpha-methl-naphthalene (C11H10 , low ignition quality).
Petroleum Refinery

## Slide 22: 3) Heating Oils No.1 fuel oil is very similar to kerosene but has a higher pour point and end point. Limiting specification are Distillation, pour point, flash point and sulfur content. No.2 fuel oil is very similar to No. 2 diesel fuel, contains cracked stock, and is blended from naphth, kerosine,diesel and cracked- cycle oils. Limiting specification are Sulfur content ( 0.25 to 0.5% max. ) Pour point ( -10 to +5 max. ) Distillation Flash point ( 120 oF min.)
Petroleum Refinery

## Slide 23: Aviation Turbine Fuels , ( ATF) , Jet Fuels Modern jet engines use fuel similar to kerosene. It is a most flexible fuel in its boiling range (up to 300 oC ) Important properties Pour point not higher than -30 oC Smoke point high Volatility Water content Naphtha These fractions are highly volatile and fall in the boiling range of motor spirits. These are mostly used as solvents in paints, perfumery and other industries.
Petroleum Refinery

## Slide 24: Solvent grades are produced by distilling wide cut naphthas into small boiling range cuts. Naphthas are not suitable for combustion because of the rapid flame propagation, resulting in explosions. Cuts boiling below 80 oC donot have any aromatics, hence their solvent power is also less, such fractions are sent for cracking operations. 80-120 oC fraction is reformed to produce an improvrd octane No. and this goes as a blend into SRG.
Petroleum Refinery

## Slide 25: Kerosenes Approx. boiling point range (150-250 )oC Low viscosity Good degree of refinement to be fairly stable. Light in color Free from smoke Used as illuminating oil. Diesel Fuels Boiling point range 250-320 oC Mainly two types : classification of diesel oils is done according to speed and load of the engine as 1) high speed diesels. 2) low speed diesels.
Petroleum Refinery

## Slide 26: Lube Oils The principal source of lubricating oil is the fraction that is left after components, namely : Gasoline, kerosene, diesel oil during crude distillation. Boiling point >350 oC Obtained from vacuum distillation units. Residuum’s after precipitation of asphaltenes are known as bright stocks and form good source for lube oils.
Petroleum Refinery